## Slide 1
TPU Inference on Google Cloud
Generations, native precision, topologies, capacity and price, measured on 65 Gemma 4 serving rigs across v5e, v6e and v5p
October 2026

## Slide 2: Executive summary
1
Match the format to the silicon. int8 W8A8 serves Gemma 4 E2B 1.7x faster than bf16 on v5e. fp8 becomes a compute format only with TPU7x.
2
v6e-1 beats the L4 on the same checkpoint. 3.3x the output tokens and 3x the KV cache on a 26B 4-bit model.
3
Capacity decides where you run. 37 zones report v6e quota; 18 have v6e-1 hardware, and full-quota zones still stock out.
4
Cold start takes 8.5 to 16.5 minutes. XLA compile is 81 to 91% of engine init, so cache it or pay it on every boot.
5
Utilization sets the price. A v5e flex-start chip costs $1.31 per million tokens at one stream and $0.09 at 64.
Source: ~/gemma4-dev rigs and docs (HARDWARE.md, QUANTIZATION.md, tpu_zones_status.md, jev-tpu-31b, tpu-vllm-v6e1-2b/v5e.md), measured Aug to Oct 2026.

## Slide 3
01
Background and history
Ten years of TPUs, and the software path that serves models on them today

## Slide 4: Google built the first TPU for inference in 2015; Ironwood (2025) puts inference first again
2015
TPU v1
Inference only, 8-bit, 92 TOPS. Announced 2016
2017
TPU v2
bf16 training, 180 TFLOPs per device, first pods
2019
TPU v3 pods
Liquid cooled, 1,024 chips, public beta
2021
TPU v4
Optical circuit switches, 4,096 chips
2023
v5e and v5p
Cost-optimized v5e; v5p with 95 GiB HBM
2024
v6e Trillium
4.7x v5e peak compute
2025
TPU7x Ironwood
fp8, 192 GiB HBM. GA March 2026
2026
TPU 8t and 8i
Announced April 2026; 8i for inference
Orange marks the inference-first chips. v1 ran 8-bit inference only; Google launched Ironwood as its “first TPU for the age of inference”.
Sources: Google Cloud blog 2016-05-19, 2017-05-17, 2019-05-08, 2023-08-29, 2023-12-06, 2024-05-15; blog.google 2021-05-19, 2025-04-09, 2026-04-22; Jouppi et al., arXiv 1704.04760; TPU release notes.

## Slide 5: vLLM reaches the TPU through tpu-inference, a JAX backend that XLA compiles per input shape
Client OpenAI-compatible HTTP API
vLLM Scheduler, batching, KV cache paging
tpu-inference JAX model code; PyTorch path as fallback
XLA Compiles one program per input shape
TPU VM Compute Engine or GKE, 1 to 8 chips per host
tpu-inference v0.31.0 shipped 2026-10-08. v5e, v6e and v7x are recommended; v5p is experimental.
Gemma 4 E2B, E4B, 26B-A4B and 31B pass its release matrix.
Compile is 81 to 91% of engine start on v6e and v5e for E2B.
Pin an image digest. The moving nightly tag broke two 4-bit builds on 2026-10-02.
Sources: github.com/vllm-project/tpu-inference (release matrix updated 2026-08-27); compile 329 of 404 s (v6e-1) and 738 of 814 s (v5e-1), tpu-jax-v5e1-2b and tpu-vllm-v5e1-2b reports; gemma4-dev/CLAUDE.md.

## Slide 6
02
Families, generations and native precision
What each chip computes natively, and what that means for quantized serving

## Slide 7: TPU7x carries about 13x the HBM of v5e at 10x the hourly price
Chip | HBM per chip | Peak bf16 | Native low precision | Max pod | On-demand
v5e | 16 GB | 197 TFLOPs | int8, 393 TOPs | 256 | $1.20/hr
v6e Trillium | 32 GB | 918 TFLOPs | int8, 1,836 TOPs | 256 | $2.70/hr
v5p | 95 GiB | 459 TFLOPs | int8; fp8 at bf16 rate | 8,960 | $4.20/hr
TPU7x Ironwood | 192 GiB | 2,307 TFLOPs | fp8, 4,614 TFLOPs | 9,216 | $12.00/hr
Single-host shapes used here: v5litepod-1 and -4, v6e-1, -4 and -8. The smallest v5p slice is v5p-8 (4 chips, quota counted in cores).
v6e on-demand varies by region: $2.70 in us-east, $2.97 in europe-west4, $3.24 in europe-west2.
Sources: docs.cloud.google.com/tpu/docs v5e, v5p, v6e, tpu7x and cloud.google.com/tpu/pricing, retrieved 2026-10-12; regional rates from Billing Catalog, gemma4-dev/HARDWARE.md:51,73-75.

## Slide 8: Only int8 on v5e and v6e, and fp8 on TPU7x, buy compute; other formats widen to bf16 first
v5e
v6e
v5p
TPU7x
bf16
native
native
native
native
int8
2x bf16
2x bf16
native
native
fp8
storage
storage
= bf16 rate
2x bf16
int4
storage
storage
storage
storage
“2x bf16” is a native matmul path at double the bf16 peak, the only real speedup.
“storage” saves HBM and bandwidth, then dequantizes to bf16 before every matmul.
The fused 4-bit kernel (gmm_v2) runs only when the quant group is narrower than the MXU: 128 columns on v5e, 256 on v6e.
fp8 KV cache on v6e logs fp8 but allocates bf16.
Sources: gemma4-dev/HARDWARE.md:13-30 (Google peak tables checked 2026-08-10); QUANTIZATION.md:86-88, 246-249, 374-378. TPU7x int8 and fp8 from docs.cloud.google.com/tpu/docs/tpu7x; less directly verified in the rigs.

## Slide 9: On v5e, int8 serves Gemma 4 E2B 1.7x faster than bf16, and fp8 trails int8
Chart: Output tok/s, one stream, v5e-1
| bf16 | 4-bit QAT | fp8 | fp8 + 4-bit emb. | int8 W8A8 | int8 + 4-bit emb.
tok/s | 144 | 150 | 182 | 203 | 220 | 243
Accuracy holds: 0.683 for bf16 against 0.677 for int8 + 4-bit embeddings on a 3,880-record suite.
Same at 12B: fp8 serves 518 tok/s at 16 streams against 624 for int8, 17% slower at the same file size.
12B int8 (11.31 GiB) is the largest model served on one 16 GB v5e chip.
Source: gemma4-dev/QUANTIZATION.md:606-645, vLLM 0.29.1rc1 on vllm-tpu, measured 2026-09-29/30. 4-bit QAT row is q4w4a16emb4.

## Slide 10: On v6e, the fused 4-bit kernel doubles 26B throughput over fp8 and holds 15.6x the KV cache
Chart: Gemma 4 26B-A4B on v6e-1, output tok/s
| fp8 dynamic | 4-bit QAT W4A16
tok/s | 668 | 1283
17.43 GiB
4-bit weights, against 27.99 GiB for fp8
53,888
KV tokens, against 3,456 for fp8
Accuracy: 75.3% for 4-bit, 76.0% for fp8.
Without the fused kernel, 4-bit served at 0.3 to 0.6x bf16.
The stock image refuses W4A16 (NotImplementedError); it took tpu-inference PRs #3299, #3653 and #3660.
Source: gemma4-dev/QUANTIZATION.md:208-213, 232, 352-355; 16 concurrent requests x 256 tokens, measured 2026-09-26.

## Slide 11
03
Topologies and slices
Which slice each Gemma 4 size needs, and when more chips stop helping

## Slide 12: Single-host slices serve every Gemma 4 size; weight size picks the slice
Model | v5e-1 (16 GB) | v6e-1 (32 GB) | v6e-4, TP=4 | v6e-8
E2B, E4B | bf16 or int8 | bf16 | — | —
12B | int8 or 4-bit | bf16 (22.18 GiB) | — | —
26B-A4B | 4-bit, 201 tok/s, 30 min boot | 4-bit, 1,283 tok/s | bf16, 1,982 tok/s | —
31B | does not fit | 4-bit, 500 tok/s | bf16, 2,031 tok/s¹ | planned, unmeasured
Topologies: v5litepod-4 is 2x2, v6e-8 is 2x4, v5p-8 is 2x2x1. Every rig here is one host.
31B bf16 needs 4+ chips: 57.7 GiB of weights against 31.24 GiB usable per v6e chip.
Throughput at 16 concurrent requests. ¹ at 256 concurrent, 32-token prompts. Sources: gemma4-dev/QUANTIZATION.md:240, 301-303, 359-365; MODELS.md:676-682, 739-756; gce-vllm-v6e8-31b REPORT 2026-08-25; HARDWARE.md:185, NAMING.md:220-225.

## Slide 13: Small models scale out: four one-chip E2B engines beat TP=4 by 3.4x at 256 streams
Chart: E2B on v5e-4: 4 engines x 1 chip, output vs one TP=4 engine
| 16 streams | 64 streams | 256 streams
ratio | 1.39 | 2.52 | 3.36
Why: E2B has one KV head. It cannot shard, so TP=4 holds four copies of the KV cache.
Bigger models do gain: 12B at TP=4 on v5e-4 serves 2.25x the v5e-1 output at one stream and 1.70x at 16.
And hold more context: 122,624 KV tokens against 9,728 on one chip.
Source: gemma4-dev/HARDWARE.md:152-168, MODELS.md:241-242, tpu-vllm-v5e4-12b-w8a8emb4/README.md:33-35; measured 2026-10-02.

## Slide 14
04
Against other accelerators
GCP L4 and Blackwell, then CUDA, AMD ROCm and AWS Inferentia

## Slide 15: On the same 26B 4-bit checkpoint, a v6e-1 serves 3.3x the tokens of a GCP L4
Chart: Output tok/s, 16 streams x 256 tokens
| NVIDIA L4 | TPU v6e-1
tok/s | 393.7 | 1283.3
3.0x
KV cache: 53,888 tokens against 17,990
58 s vs 139 s
3,880-record suite, v6e-1 against L4
Same checkpoint, flags and client; different kernels: gmm_v2 on TPU, Marlin on L4.
The L4 ran stock vLLM 0.30.0; the TPU needed three tpu-inference patches.
List price per hour: v6e $2.70, L4 (g2-standard-4) $0.71.
Sources: jev-tpu-31b/results/2026-09-26-moe2-evidence/run.log:165 and 2026-09-26-gpu-l4-evidence/run.log:167 (L4 on g2-standard-8); QUANTIZATION.md:388-394; prices cloud.google.com, retrieved 2026-10-12.

## Slide 16: Blackwell on GCP costs more per hour than v6e; none of these rigs has measured it
Accelerator | Machine type | On-demand | Flex-start | Measured here
NVIDIA L4 | g2-standard-4 | $0.71 | — | Yes
TPU v5e | ct5lp-hightpu-1t | $1.20 | $0.60 | Yes
TPU v6e | ct6e-standard-1t | $2.70 | $1.35 | Yes
RTX PRO 6000 (Blackwell) | g4-standard-48 | $4.50 | $2.25 | No
B200 (Blackwell), per GPU | a4-highgpu-8g ÷ 8 | not offered | $8.06 | No
TPU7x Ironwood | tpu7x-standard-4t | $12.00 | $6.00 | No
Per accelerator-hour. Blackwell adds fp4 arithmetic; Google's TPU7x docs list bf16 and fp8 only, and TPU7x is the first TPU with fp8 math.
Sources: cloud.google.com/products/compute/pricing/accelerator-optimized (us-central1) and cloud.google.com/tpu/pricing, retrieved 2026-10-12; fp4 note gemma4-dev/QUANTIZATION.md:943; fp8 HARDWARE.md:18.

## Slide 17: On E2B bf16, MI300X leads raw speed, and v5e at spot price leads tokens per dollar to 16 streams
Chart: Output tok/s per $ per hour
| 1 stream | 4 streams | 16 streams | 64 streams
AMD MI300X ($1.99) | 153 | 487 | 1333 | 2713
TPU v5e-1 spot ($0.58) | 208 | 711 | 1572 | 1972
TPU v6e-1 ($2.97) | 67 | 233 | 587 | 719
Raw speed, one stream: MI300X 305, v6e 199, v5e 120, L4 46 tok/s.
L4 at spot ($0.94): 49 and 187 tok/s per $ per hour at 1 and 4 streams.
At list prices (v5e $1.20), MI300X returns 1.4 to 2.9x v5e's tokens per dollar.
Different vLLM builds, hosts and repeat counts per platform; read as direction, not an A/B result. MI300X on DigitalOcean, L4 on AWS g6.2xlarge. Source: gpu-vllm-mi300x-2b/devto-gemma4-mi300x-dollar-hour.md:200-223; vllm bench serve, 1024 in / 128 out.

## Slide 18: Each software stack fails in its own way: TPU compiles longest, Neuron can fail silently
 | TPU (vLLM + JAX) | CUDA (L4) | ROCm (MI300X) | Neuron (inf2, trn1)
Start to healthy, E2B | 510 s v6e, 986 s v5e | 334 s | about 160 s | 171 s on trn1
E2B tok/s, 1 stream | 199 v6e, 120 v5e | 46 | 305 | 44 to 61 on inf2¹
Gemma 4 support | 4-bit needed patches | 26B 4-bit loads stock | fp8 only as fnuz | vLLM-Neuron cannot load it
Hazard | OOM after a long compile | sm_89 missing; runs sm_86 code | AITER flag 0.97 to 0.99x | Large gather returns zeros, HTTP 200
¹ Custom client, not vllm bench. Sources: tpu-vllm-v5e1-2b and tpu-jax-v5e1-2b reports; gpu-vllm-g6-2b report 2026-08-30; devto-gemma4-mi300x-dollar-hour.md:247; HARDWARE.md:645-683, 722-749; tpu-vllm-trn1-2b smoke REPORT 2026-10-05; tpu-pytorch-inf2-2b/README.md:102-105.

## Slide 19
05
Production gotchas
Capacity, control planes, cold start and serving flags

## Slide 20: Quota is not availability: a create must pass three gates, and quota is the weakest
1. Hardware in the zone
37 zones report v6e quota. Only 18 offer v6e-1 hardware; Google's docs list 8.
2. Provisioning model offered
us-central1-b has hardware, quota and a flex-start price, and rejects flex-start. v5e flex-start: 1 zone of 44.
3. Capacity right now
3 of 5 zones holding 1,536 chips of quota returned stockout. One granted, then stocked out a minute later.
Probe with spot, not flex-start. A flex-start create with no quota queues as PENDING, exactly like a stockout; spot fails fast with “reason: stockout”.
Sources: gemma4-dev/tpu-vllm-v6e1-2b/tpu_zones_status.md:15-50 (2026-08-10); TPU.md:286-299; request-quota.sh:40-43 (verified 2026-08-11).

## Slide 21: Ask for fewer chips: 8 v6e chips expired after 26 minutes where 4 were granted at once
Request | Where | Outcome
v6e-1 flex, Compute Engine | — | Running in 105 s
v5e-1 flex-start | us-west4-a | Granted within 2 min
v6e-1 flex-start, GKE | europe-west4 | Granted in 4 min 18 s
v6e-1 flex-start | europe-west4-a | No capacity after 30 min
v5e-1 flex-start | us-west4-a | Cancelled after 1 h 22 min
v6e-8 flex-start | europe-west4-a | Expired after 26 min
v6e-8 spot | us-central1-b | Preempted at about 6 min
v6e-4 flex-start | europe-west4-a | Granted instantly
Same zone, same hour: 8 chips stocked out and 4 were granted under an hour later.
Keep queued requests. Flex-start capacity has taken up to 2 hours, with no published SLA.
Quota itself came fast: automated decisions in seconds, approved in two regions and denied in three.
Sources: gce-vllm-v6e8-31b REPORT 2026-08-25:111-119; jev-tpu/PREREGISTRATION.md:59; jev-tpu-v5e1/PREREGISTRATION.md:143; gke first-provision README:108; gce-jaxrust-v6e1-2b article:97; CLAUDE.md:114; TPU.md:259-283.

## Slide 22: The control plane is changing, and most of its failures are quiet
Cloud TPU API is frozen
Bug fixes only. TPU7x runs only on Compute Engine or GKE.
v5e has no Compute Engine path
Listed in 26 zones; create refused for this user agent.
Two disjoint quota pools
us-east5: 512 v6e chips via the TPU API, 0 via Compute Engine.
RUNNING means booted
A GKE node is Ready about 10 min before the model serves.
Boot defaults break vLLM
10 GB disk, no Docker on PATH; a missing scope spins 30 min.
Nothing stops billing
GKE pools and old queued resources bill until deleted.
Sources: docs.cloud.google.com/tpu/docs (TPU API notice); gemma4-dev/TPU.md:15-19, 99-112, 181-191, 307-375; request-quota.sh:7-10; gke-vllm-v6e1-2b/CLAUDE.md:76-77, 263-315; gce-vllm-v5e1-2b/CLAUDE.md:151-152.

## Slide 23: XLA compile is most of a cold start, so cache it and stage weights in-region
Chart: Seconds from container start to healthy
| v6e-1, E2B | v5e-1, E2B
XLA compile | 329 | 738
Everything else | 181 | 248
−42%
v5e restart with a mounted compile cache, 857 to 497 s
5.6 min
31B weights from in-region GCS, against 60 to 90 min from Hugging Face
GKE from nothing to first token took about 28 min: cluster 12, node pool 6, model 10.
The default compile cache (197 MB) lives inside the container and dies with docker rm.
A cold start costs money: $0.19 to $0.24 per v6e boot at flex-start rates.
Sources: tpu-jax-v5e1-2b report 2026-07-21:197-209 (v6e); tpu-vllm-v5e1-2b report 2026-08-06:903-905 and SERVING-PARAMS.md:77-78; gce-vllm-v6e8-31b REPORT:100-103; gke first-provision README:25-29; tpu-pytorch-v6e1-2b/devto-post.md:128.

## Slide 24: Serving flags that work on GPUs fail late on TPU, often after a full compile
--gpu-memory-utilization 0.95
Failed on v5e after a 691 s compile, twice. 0.92 serves.
--max-num-batched-tokens
vLLM applied generic defaults (2048/256) silently. Gemma 4 needs 2,496 or the server refuses to start.
--kv-cache-dtype fp8
On v6e it logs fp8 and allocates bf16. On v5e 12B it doubled KV tokens, 9,728 to 18,944.
Scoped VMEM, 115.2 MB per kernel
A 12B 4-bit layer needed 117.6 MB; it served after lowering the tile fraction to 0.85.
vllm/vllm-tpu:nightly
Broke two 4-bit QAT builds at model load on 2026-10-02. Pin a digest.
Sources: gemma4-dev/tpu-vllm-v5e1-2b/SERVING-PARAMS.md:42; tpu-vllm-v6e1-2b/SERVING-PARAMS.md:216-233; QUANTIZATION.md:374-378, 1149-1155; HARDWARE.md:115-118; MODELS.md:701; CLAUDE.md:25-27.

## Slide 25
06
Pricing
List rates by provisioning model, and what a million tokens costs in practice

## Slide 26: Flex-start halves on-demand on every generation; a 3-year commitment cuts it 55%
$ per chip-hour | On-demand | Flex-start | Calendar | 1-yr CUD | 3-yr CUD | Spot read
v5e | $1.20 | $0.60 | $0.84 | $0.84 | $0.54 | $0.58
v6e Trillium | $2.70 | $1.35 | $1.89 | $1.89 | $1.22 | $1.40
v5p | $4.20 | $2.10 | $2.94 | $2.94 | $1.89 | —
TPU7x Ironwood | $12.00 | $6.00 | $8.40 | $8.40 | $5.40 | —
Flex-start can undercut spot: v6e in us-east5 lists $1.35 flex-start against $1.40 spot.
Flex-start runs 10 min to 7 days and bills until deleted; v6e flex-start is published in 8 regions.
TPU7x spot, flex-start and calendar are behind an allowlist.
List rates: cloud.google.com/tpu/pricing, retrieved 2026-10-12 (v5e and TPU7x us-central1; v6e and v5p us-east1/us-east5). Spot: Billing Catalog reads, v5e us-west4 2026-08-06, v6e us-east5 (HARDWARE.md:75). TPU.md:77, 377; HARDWARE.md:382.

## Slide 27: Idle capacity sets the price: one stream costs 7.5x more per token than 32 on v6e
Chart: v6e-1 E2B, $ per million output tokens at $2.97/hr
| 1 stream | 8 streams | 32 streams
$/M | 4.14 | 0.7 | 0.55
v5e at flex-start ($0.60): $1.31 per million at one stream, $0.09 at 64, a 14.8x spread.
26B on v6e-1: 4-bit $0.29 flex-start or $0.64 on-demand; fp8 $0.56 or $1.23.
Break-even with Gemini 2.5 Flash-Lite ($0.40/M) needs about 940 tok/s sustained on a flex-start v6e.
Chip cost only. Sources: gke-vllm-v6e1-2b first-provision README:85-89 (2026-08-25); tpu-vllm-v6e1-2b/v5e.md:304-318; jev-tpu-31b/results/2026-09-26-26b-ARTICLE-FIGURES.md:101-104; tpu-pytorch-v6e1-2b/devto-post.md:126.

## Slide 28: Bills grow from meters nobody watches: idle pools, side fees and stale rate tables
Flex-start bills until deleted
The rigs cap runs at 4 hours with --max-run-duration instead of the 7-day maximum.
GKE adds two meters
System node plus cluster fee: $0.2475/hr, about $181 a month before any chip.
Slices bill per chip
A v6e-8 at flex-start is $10.80/hr; a 4-hour cap is about $43.
Catalog names hide the model
Flex-start is sold as “DWS Defined Duration”; spot as “attached to Spot Preemptible VMs”.
Rate tables go stale
One rig hardcoded v5e at $0.12/hr against a $1.20 list rate, 10x off.
Rejected creates are free
A refused or stocked-out create bills nothing; a preempted spot VM bills its minutes.
Sources: tpu-pytorch-v6e1-2b/devto-article.md:30; tpu-vllm-v6e1-2b/v5e.md:322; gke-vllm-v6e1-2b/CLAUDE.md:353 and first-provision README:115-116; gce-vllm-v6e8-31b/DEPLOY.md:79-80; tpu-vllm-v5e1-2b/CLAUDE.md:233-239; HARDWARE.md:430; jev-tpu/evidence-v6e1/cost.txt.

## Slide 29: So, which one?
Workload | Pick | Why
E2B or E4B, cost first | v5e-1, int8 W8A8, one engine per chip | 1.7x bf16 speed; lowest $/M at spot or flex-start
12B to 31B on one chip | v6e-1, 4-bit QAT W4A16 | 26B at 1,283 tok/s; 31B fits in 21.67 GiB
bf16 26B or 31B, long context | v6e-4, TP=4 | ~2,000 tok/s and 235K KV tokens at 26B
fp8 compute, 192 GiB per chip | TPU7x | Only TPU with fp8 math; allowlisted, unmeasured here
Stock software, fast boot | L4 or MI300X | L4 loads 26B 4-bit unpatched; 160 to 334 s to healthy
For any of them: probe capacity with spot, ask for the smallest slice that fits, pin the image digest and mount the compile cache.

## Slide 30: Sources
Measured rigs and notes: ~/gemma4-dev (git, last commit 2026-10-11): HARDWARE.md, QUANTIZATION.md, MODELS.md, TPU.md, NAMING.md, request-quota.sh, tpu-vllm-v5e1-*, tpu-vllm-v5e4-*, tpu-vllm-v6e1-2b, gce-vllm-v6e*, gke-vllm-v6e1-2b, jev-tpu, jev-tpu-31b, gpu-vllm-g6-2b, gpu-vllm-mi300x-2b, tpu-pytorch-inf2-2b, tpu-*-trn1-2b.
Google documentation, retrieved 2026-10-12: docs.cloud.google.com/tpu/docs (v2, v3, v4, v5e, v5p, v6e, tpu7x, release notes); cloud.google.com/tpu/pricing; cloud.google.com/spot-vms/pricing; cloud.google.com/products/compute/pricing/accelerator-optimized.
History: Google Cloud blog posts dated 2016-05-19, 2017-05-17, 2019-05-08, 2019-08-23, 2023-04-05, 2023-08-29, 2023-12-06, 2024-05-15; blog.google 2021-05-19, 2025-04-09, 2026-04-22; cloud.google.com/transform TPU history (2024-07-31); Jouppi et al., In-Datacenter Performance Analysis of a TPU, arXiv 1704.04760.
Software: github.com/vllm-project/tpu-inference, v0.31.0 (2026-10-08). AWS inf2.xlarge rate from the AWS Pricing API, effective 2026-10-01.